## Slide 1
VOICE CONVERSION USING MATLAB
AIM OF OUR PROJECT :
To produce the words of one person (source speaker) in the voice of another person (target speaker).

## Slide 2
Identifiers between different speakers :
Vocal tract transfer function
Pitch range
Every person’s distinct vocal qualities are mainly caused by their vocal tract, which forms a transfer function between the input excitation and the output speech.
We can isolate this transfer function using cepstral analysis.
The second major identifier is the pitch range of the words of a speaker. We can change the pitch using available algorithms.

## Slide 3
The output of a system is the convolution of the input sequence with the system response.
Speech, the output signal coming out from a system is considered as the convolution of the input excitation and vocal tract filter characteristics.
S(n) = e(n) * h(n)
The objective of cepstral analysis is to separate the speech into its source and system components without any prior knowledge about its source or vocal components.
In frequency domain, S(w) = E(w) H(w) (using DFT)
To deconvolve the speech signal into excitation and vocal tract components in time domain, this multiplication has to be converted into a linear combination of these two components. This is done using log operation.
log|S(w)| = log|E(w)| + log|H(w)|
The separation can be done by taking IDFT of the linearly combined log spectra of excitation and vocal tract components.

## Slide 4
CEPSTRAL DOMAIN :
IDFT of log spectra transforms back to quefrency domain or cepstral domain (not to time domain).
c(n) = IDFT (log|S(w)|) = IDFT (log|E(w)|) + IDFT ( log|H(w)|)
In cepstral domain,
Vocal tract components are represented by the slow varying components concentrated near the low quefrency region.
Excitation components are represented by the fast varying component at the high quefrency region.
As the spectrum of any given signal is symmetric and the cepstrum is derived from the log magnitude of the linear spectrum, therefore, it is also symmetrical in cepstral domain.

## Slide 5
Speech is a non- stationary signal i.e. the frequency components change with time.
To be more specific, a particular set of frequency component is present in one interval and another set of frequency components in some other interval and so on.
To take care of time varying spectral information, the short term processing approach is employed. In this, speech is processed in blocks of 10-30 ms with a shift of 10 ms. In this short frame, it remains time invariant. For this purpose, we multiply it with a window.
Window- method : Long signal (of speech or ideal impulse response) is multiplied with a window function of finite length, giving finite length weighted version of original signal.
In speech processing, usually some soft window like Hamming, Hanning, triangle, etc. is used to reduce the sidelobes substantially.

## Slide 6
LIFTERING :
Liftering operation is similar to filtering operation in frequency domain where a desired quefrency region for analysis is selected by multiplying the whole cepstrum by a rectangular window at the desired position.
Types : low time liftering and high time liftering
Low time liftering operation is performed to extract the vocal tract characteristics in the quefrency domain.
High time liftering is performed to get the excitation characteristics of the analysis speech frame.

## Slide 7
Cepstral analysis :
Sound signal
Window
abs(DFT)
Log
IDFT
Cepstral liftering
Transfer function Excitation
(low quefrency) (high quefrency)

## Slide 8
High- time liftering for pitch estimation :
As the cepstrum computed is symmetric, half the length of cepstrum is considered for liftering.
Pitch can be estimated as the instant corresponding to the highest peak in the high- time liftered cepstrum.
Pitch period is the time instant corresponding to the largest peak in the high- time liftered cepstrum.
The reciprocal of the pitch period multiplied by the sampling frequency gives the pitch frequency of the speech frame under analysis.

## Slide 9
Pitch shift :
Use resampling to increase or decrease sound pitch by desired amount. Because resampling modifies both sound duration and pitch in the same ratio, the sound duration will become different than original in the process.
The adjust the sound duration modified by bringing back to the original duration by using some algorithms. The result has the same duration as original, but now with desired pitch.

## Slide 10
Why do we need voice conversion ?
Voice dubbing in movies
Foreign language training
Cross language rap singing